Xmas Lights Controller
# Hardware
## Power Supply
A 5m string of 5050 LEDs (300 RGB LEDs) requires (continuous) R=0.9A, G=0.7A, B=0.6A.

The intended power supply is a PC ATX, supplying both 12V and 5V. In this case. The LDO1 and C11 should be omitted; they are only required if a single supply at 12V is to be used.

# Firmware
## Functional Description
### Inputs and LFO
### Trigger/Gate Mask
## EEPROM – Saved Programs
In the following, [nn] indicates the number of bytes. NB: see the doxygen documentation for definitive #defines.
EEPROM Header:
- Number of leds [1] => indicates program size
- {unused} [7]
Following the header, 1..* programs consisting of nnn Bytes (nnn depends on number of LEDs) arranged in blocks:
- LFO setting [4]
- Trigger gate mask [4]
- LED shape (repeated for each LED) [4 per LED]
- LED patch definition (repeated for each LED) [4 per LED]
=> for 9 LEDS need 80 bytes (25 programs in 2k EEPROM), or for 3 LEDS need 32 bytes (63 programs in 2k EEPROM)

LFO setting:
- Rate [1]
- {not used} [3]

Trigger/gate mask:
- Rate [1]
- Pattern [1] – see #define TGM_*
- {not used} [2]
#define TGM_DISABLED 0 //no not use trigger gate mask (this is not strictly necessary since, TGM only has effect if relevant elements in srcVals are patched to a LED controller
#define TGM_SINGLE 1 //single bit on
#define TGM_GROW 2 //bits progressively turn on to MSB then turn off from MSB
#define TGM_PASS 3 //bits progressively turn on to MSB then turn off from LSB
#define TGM_DOUBLE 4// like SINGLE 2 bits on
#define TGM_TRIPLIFY 128 //add this to treat the change pattern as an RGB pattern and replicate across all RGB triples

LED Shape:
- Shape [1] – see #define SBC_WAVESHAPE_*
- {not used}
- Phase [2] – byte order H,L (120 deg=0x2AA, 240 deg=0x554)
#define SBC_WAVESHAPE_OFF 0 //!< The LED is always off, for the whole period
#define SBC_WAVESHAPE_SAW 1 //!< Ramping up saw tooth
#define SBC_WAVESHAPE_TRI 2 //!< Triangle
#define SBC_WAVESHAPE_SQU 3 //!< Square 50/50 mark/space
#define SBC_WAVESHAPE_PULSE 4 //!< 20/80 mark space pulse wave
#define SBC_WAVESHAPE_HUMP 5 //!< Rounded top hump (not quite sine)
#define SBC_WAVESHAPE_SPIKE 6 //!< Accelerating rise and fall (spikier than a triangle)
#define SBC_WAVESHAPE_ON 7 //!< The LED is always on, for the whole period
SBC_WSMOD_*
Various ways of modifying the waveform shape as set by SBC_WAVESHAPE_* - add to it to create bit-mask to pass to setPattern()
#define SBC_WSMOD_INVERT 8 //!< The output is flipped.
#define SBC_WSMOD_MISS1 16 //!< after one cycle of the wave shape (determined by the internal counter), spend one cycle waiting
#define SBC_WSMOD_MISS2 32 //!< after one cycle of the wave shape (determined by the internal counter), spend two cycles waiting
SBC_TG_*
Control trigger/gate behaviour - add to SBC_WAVESHAPE_* to create bit-mask to pass to setPattern(). SBC_TG_1SHOT takes priority
#define SBC_TG_GATECHANGE 0 //!< This is default behaviour; the trigger/gate input will determine whether the LED brightness will change. (if no gate input, it remains fixed at the last value)
#define SBC_TG_GATEOUT 64 //!< The Trigger/gate input over-rides the output. If below threshold then the LED will be off, otherwise as controlled by the waveshape/rate/etc.
#define SBC_TG_1SHOT 128 //!< The output will stay off (or on, if SBC_INVERT) until the trigger intput >=512. Phase is irrelevant in this mode.

LED Patch
- Rate control source [1] – see #define SRC_*
- Rate factor [1]
- Brightness max (scale) source [1] – see #define SRC_*
- Trigger/gate source [1] – see #define SRC_*

#define SRC_OFF 0 //permanently OFF, i.e. value = 0
#define SRC_ON 1 //always ON, i.e. value =1023
#define SRC_AUDIO 2 //audio level (ADC0)
#define SRC_LEV1 3 //VR1 (ADC1)
#define SRC_LEV2 4 //VR2 or thermister (ADC2)
#define SRC_LEV3 5 //VR3 or LDR (ADC3)
#define SRC_SW1 6 //switch 1
#define SRC_SW2 7 //switch 2
#define SRC_SW3 8 //switch 3
#define SRC_IR_INT1 9 //IR controlled integer value #1
#define SRC_IR_INT2 0xA //IR controlled integer value #2
#define SRC_IR_INT3 0xB //IR controlled integer value #3
#define SRC_LFO 0xE //Low Freq osc (triangle wave)
#define SRC_RND 0xF //Random number in range 0-1023
#define SRC_TG_MASK_BASE 0x10 //srcVals index at which the trigger/gate mask values reside (there are SBC_NUM_LEDS of them).
//NB TG_MASK is, in principle, available for rate and scale patches, but is NOT intended for use that way