Xmas Lights Controller
# Hardware
## Power Supply
A 5m string of 5050 LEDs (300 RGB LEDs) requires (continuous) R=0.9A, G=0.7A, B=0.6A.

The intended power supply is a PC ATX, supplying both 12V and 5V. In this case. The LDO1 and C11 should be omitted; they are only required if a single supply at 12V is to be used.

# Firmware
## Functional Description
### Inputs and LFO
### Trigger/Gate Mask
## EEPROM
### Saved Program Format
In the following, [nn] indicates the number of bytes. NB: see the doxygen documentation for definitive #defines.
EEPROM Header (starts at EEPROM address = 0):
- Number of leds [1] => indicates program size
- Number of programs available [1]
- {unused} [6]
NB: the number of LEDS stored at address=0 MUST match the number of LEDS in source code (#define NUM_LEDS). Otherwise, on boot the EEPROM is over-written at addresses 0 and 1 with NUM_LEDS and 0 respectively.
Following the header, 1..* programs consisting of nnn Bytes (nnn depends on number of LEDs) arranged in blocks:
- LFO setting [4]
- Trigger gate mask [4]
- LED shape (repeated for each LED) [4 per LED]
- LED patch definition (repeated for each LED) [4 per LED]
=> for 9 LEDS need 80 bytes (25 programs in 2k EEPROM), or for 3 LEDS need 32 bytes (63 programs in 2k EEPROM)

LFO setting:
- Rate [1]
- {not used} [3]
Trigger/gate mask:
- Rate [1] – a value of 0x80 gives a rate of about 1 change per second.
- Pattern [1] – see #define TGM_*
- {not used} [2]
LED Shape:
- Shape [1] – see #define SBC_WAVESHAPE_*
- {not used}
- Phase [2] – byte order H,L (120 deg=0x2AA, 240 deg=0x554)
LED Patch
- Rate control source [1] – see #define SRC_*
- Rate factor [1]
- Brightness max (scale) source [1] – see #define SRC_*
- Trigger/gate source [1] – see #define SRC_*
### Program Byte Values
T/G Mask
#define TGM_DISABLED 0 //no not use trigger gate mask (this is not strictly necessary since, TGM only has effect if relevant elements in srcVals are patched to a LED controller
#define TGM_SINGLE 1 //single bit on
#define TGM_GROW 2 //bits progressively turn on to MSB then turn off from MSB
#define TGM_PASS 3 //bits progressively turn on to MSB then turn off from LSB
#define TGM_DOUBLE 4// like SINGLE 2 bits on
#define TGM_TRIPLIFY 128 //add this to treat the change pattern as an RGB pattern and replicate across all RGB triples

Shape
#define SBC_WAVESHAPE_OFF 0 //!< The LED is always off, for the whole period
#define SBC_WAVESHAPE_SAW 1 //!< Ramping up saw tooth
#define SBC_WAVESHAPE_TRI 2 //!< Triangle
#define SBC_WAVESHAPE_SQU 3 //!< Square 50/50 mark/space
#define SBC_WAVESHAPE_PULSE 4 //!< 20/80 mark space pulse wave
#define SBC_WAVESHAPE_SPIKE 5 //!< Accelerating rise and fall (spikier than a triangle)
#define SBC_WAVESHAPE_RND 5 //!< Intensity changes randomly once per cycle
#define SBC_WAVESHAPE_ON 7 //!< The LED is always on, for the whole period

SBC_WSMOD_*
Various ways of modifying the waveform shape as set by SBC_WAVESHAPE_* - add to it to create bit-mask to pass to setPattern()
#define SBC_WSMOD_INVERT 8 //!< The output is flipped.
#define SBC_WSMOD_MISS1 16 //!< after one cycle of the wave shape (determined by the internal counter), spend one cycle waiting
#define SBC_WSMOD_MISS2 32 //!< after one cycle of the wave shape (determined by the internal counter), spend two cycles waiting

SBC_TG_*
Control trigger/gate behaviour - add to SBC_WAVESHAPE_* to create bit-mask to pass to setPattern(). SBC_TG_1SHOT takes priority
#define SBC_TG_GATECHANGE 0 //!< This is default behaviour; the trigger/gate input will determine whether the LED brightness will change. (if no gate input, it remains fixed at the last value)
#define SBC_TG_GATEOUT 64 //!< The Trigger/gate input over-rides the output. If below threshold then the LED will be off, otherwise as controlled by the waveshape/rate/etc.
#define SBC_TG_1SHOT 128 //!< The output will stay off (or on, if SBC_INVERT) until the trigger intput >=512. Phase is irrelevant in this mode.

Patch
#define SRC_OFF 0 //permanently OFF, i.e. value = 0
#define SRC_ON 1 //always ON, i.e. value =1023
#define SRC_HALF 2 //always value = 512
#define SRC_AUDIO 3 //audio level (ADC0)
#define SRC_LEV1 4 //VR1 (ADC1)
#define SRC_LEV2 5 //VR2 or thermister (ADC2)
#define SRC_LEV3 6 //VR3 or LDR (ADC3)
#define SRC_SW1 7 //switch 1 | IR controlled boolean #1
#define SRC_SW2 8 //switch 2 | IR controlled boolean #2
#define SRC_SW3 9 //switch 3 | IR controlled boolean #3
#define SRC_IR_INT1 0xA //IR controlled integer value #1
#define SRC_IR_INT2 0xB //IR controlled integer value #2
#define SRC_IR_INT3 0xC //IR controlled integer value #3
#define SRC_LFO 0xD //Low Freq osc (triangle wave)
#define SRC_RND_1S 0xE //Random number in range 0-1023, changing every second
#define SRC_RND_10S 0xF //Random number in range 0-1023, changing every 10 seconds
#define SRC_TG_MASK_BASE 0x10 //srcVals index at which the trigger/gate mask values reside (there are NUM_LEDS of them).
//NB TG_MASK is, in principle, available for rate and scale patches, but is NOT intended for use that way
### Unit Tests
NB: all unit tests have 3 LEDs defined in the header block, so require #define NUM_LEDS 3
Bank 1, waveform tests.
1. [addr 0x0008] One LED SBC_WAVESHAPE_ON,
   scale from VR2
2. [addr 0x0028] One LED SBC_WAVESHAPE_SAW,
   rate from VR1, scale from VR2, change gate from VR3
3. [addr 0x0048] One LED SBC_WAVESHAPE_TRI,
   rate from VR1, scale from VR2, change gate from VR3
4. [addr 0x0068] One LED SBC_WAVESHAPE_SQU,
   rate from VR1, scale from VR2, change gate from VR3
5. [addr 0x0088] One LED SBC_WAVESHAPE_PULSE,
   rate from VR1, scale from VR2, change gate from VR3
6. [addr 0x00A8] One LED SBC_WAVESHAPE_SPIKE,
   rate from VR1, scale from VR2, change gate from VR3
7. [addr 0x00C8] One LED SBC_WAVESHAPE_RND,
   rate from VR1, scale from VR2, change gate from VR3
8. [addr 0x00E8] All LEDS SBC_WAVESHAPE_OFF
9. [addr 0x0108] One LED SBC_WAVESHAPE_SAW, INVERTED,
   (VR sources as #2)
10. [addr 0x0128] One LED SBC_WAVESHAPE_SAW, MISS 1,
    (VR sources as #2)
11. [addr 0x0148] One LED SBC_WAVESHAPE_SAW, MISS 2,
    (VR sources as #2)
12. [addr 0x0168] One LED SBC_WAVESHAPE_SAW, MISS 3,
    (VR sources as #2)
13. [addr 0x0188] One LED SBC_WAVESHAPE_SAW, GATEOUT
    out gate from button 1, (VR sources for rate and scale)
14. [addr 0x01A8] One LED SBC_WAVESHAPE_SAW, 1SHOT
    one shot trigg from button 1, (VR sources as #13)
15. [addr 0x01C8] One LED SBC_WAVESHAPE_SAW, 1SHOT
    one shot trigg from button 1, MISS 2, (VR sources as #13)
16. [addr 0x01E8] One LED, TRI, 180 degree phase shifted.
17. [addr 0x0208] TRI waveform RGB, 120 degree phase separation,
    ALL rate from VR1, ALL scale from VR2
18. [addr 0x0228] SQU waveform RGB, 120 degree phase separation,
    ALL rate from VR1, ALL scale from VR2

Bank 2, patch sources and rate prescale:
1. .
2. incl LFO

Bank 3, trigger/gate mask
1. [addr 0x0008] Base is all LEDs SBC_WAVESHAPE_ON, GATEOUT, scale at HALF,
   mask pattern = SINGLE, T/G rate=0x80
2. [addr 0x0008] As #1
   mask pattern = SINGLE, T/G rate=0x40
3. [addr 0x0048] As #2
   mask pattern = GROW
4. [addr 0x0068] As #2
   mask pattern = PASS
5. [addr 0x0088] As #2
   mask pattern = DOUBLE
6. [addr 0x00A8] Base is all LEDs SBC_WAVESHAPE_SPIKE, 1SHOT, rate=VR1, scale = VR2,
   mask pattern = SINGLE, T/G rate=0x40
7. #### to do: TRIPLIFY – requires >3 LEDs
### Direct EEPROM Load of Programs
Use e.g. Tiny Hexer (mrikes.de). Hint set editor options to be 4 bytes wide to match most of the blocks (above).
Export as Intel HEX. Address records are linear starting at 0x00000000.
To get the plain hex text, export as Hex Text. Do not confuse with the Intel HEX format!
Use avrdude to upload.
C:\Program Files\Arduino\hardware\tools\avr\bin\avrdude.exe -C"C:\Program Files\Arduino\hardware\tools\avr\etc\avrdude.conf" -patmega328p -carduino -P\\.\COM5 -b115200 -Ueeprom:w:"$(ItemPath)":i
[no good if current version of optiboot present – skips EEPROM upload!]
Use ISP!
Note that opening a previously exported Intel HEX format .hex file in Tiny Hexer without importing does not give the “right answer”. i.e. to edit, use import, then change, then export.

Plain Hex for simple prog with 3 leds, all with sawtooth, connexted to VR1-VR3
03 00 00 00 //3 leds
00 00 00 00
80 00 00 00 //LFO
01 00 00 00 //TG Mask
01 00 00 00 //LED Pattern1 – saw, phase=0
01 00 02 AA //LED Pattern2 – saw, phase=120
01 00 05 54 //LED Pattern3 – saw, phase=240
04 00 01 01 //LED Patch1 – rate from VR1, scale and TG at SRC_ON
05 00 01 01 //LED Patch2 – rate from VR2, scale and TG at SRC_ON
06 00 01 01 //LED Patch3 – rate from VR3, scale and TG at SRC_ON

# IR Keypad
## Run mode
### Loading Programs From EEPROM
Method 1 – direct entry of program
Press PROG (“EQ”) then one or two numbers then OK (“200+”).
If a non-number button is pressed, it is ignored.
If more than two numbers are pressed then only the last two are used.
Program numbers start at 1. If no numbers pressed or only 0 is pressed then no program will be loaded on OK. Also no program loaded if the program number is out of range (would not fit in 2k EEPROM).
Press CANCEL (“100+”) to abort.
Method 2 – load next/previous program
Press PROG (“EQ”) then either PLUS or MINUS (“VOL+” or “VOL-”). The program loads immediately. PROG must be pressed before each use of PLUS or MINUS.